## Slide 1: Designing the Landscape
Chapter 4

## Slide 2: The Major Design Areas
The good residential landscape design has three main areas to be designed:
They are:
  The public area
  The outdoor living area
  The service area

## Slide 3: The Major Design Areas
The Public Area:
  Is the portion of the property that is in full view of the public.
  This area provides the first impression of the house.
  The front door is the most important aspect of the public area
  The front door is the focal point or point of emphasis of a well designed landscape.

## Slide 4: The Major Design Areas
Public Cont..
  The focal point will capture the attention of the viewer.
  There are three main goals to keep in mind when designing:
    Soften the architectural lines of the house
    Frame the house with trees
    Maintain the open lawn areas

## Slide 5: The Major Design Areas
Public Cont..
  walks and driveways are important items too in the public.
  Walk way will need to lead guest to the front door therefore it should follow a direct line and be wide enough for two people to walk side by side.

## Slide 6: The Major Design Areas
Public Cont..
The size of the driveway should be the following:
One car minimum of 10 feet wide
Two car should be 18 feet wide

## Slide 7: The Major Design Areas
Public Cont…
The use of trees :
  used to screen a point where brick is a different color
  large roof mounted antenna
  A satellite dish
  Awkward roof line or chimney

## Slide 8: The Major Design Areas
Public Cont..
  Shrubs are used in the public are to tie the house to the landscape.
  They soften the vertical lines of the house and hide the foundation.
  To soften of architectural lines you want to place shrubs at the foundation of the house.

## Slide 9: The Major Design Areas
Public Cont..
  Plants that are pruned in unnatural shapes do not belong in the public area.
  Examples of shrubs in green meat balls, poodle bushes and other unnatural shapes.
  If you do prune shrubs like this you are placing stress on the plants by reducing total leaf surface area.

## Slide 10: The Major Design Areas
Public Cont..
What is a corner plantings
  It is plants with round forms and arrange them in group plantings. Good rule to follow is to select plants that will not grow taller than 2/3 the distance from the ground to the eaves

## Slide 11: The Major Design Areas
Public Cont..
What is a doorway plantings?
  It is located on either side of the entry door. These plantings may be identical if the architecture of the house has formal balance
  To determine the height of these plants draw a line from the threshold of the door to a point at the corners of the house that is 2/3 the distance from the ground to the eaves

## Slide 12: The Major Design Areas
The Outdoor Living Area:
  is designed differently than the public area .
  It includes all the property to the rear of the house except the service area.
  Some landscapers also call the outdoor living area the private area.

## Slide 13: The Major Design Areas
The Outdoor Living Area :
  it is designed with the family’s gardening interest, entertainment activities,
  There are several design elements that satisfy the needs and interests of the family they are:
    Enclosures
    Surface Areas
    Plantings
    Garden Accessories

## Slide 14: The Major Design Areas
The Outdoor Living Area:
  What does Enclosure mean?
  It includes fences , walls, or plants create wall for the outdoor living room

## Slide 15: The Major Design Areas
The Outdoor Living Area:
  What does Surface area mean?
  Such as walks, paths, sitting areas, patios, and decks comprise one element of the outdoor living area.

## Slide 16: The Major Design Areas
The Outdoor Living Area:
  What does Plantings mean?
    It is the planting of shrubs , trees, perennials, annuals, and ground cover enhance the appearance of the outdoor living area

## Slide 17: The Major Design Areas
The Outdoor Living Area:
  What is Garden Accessories?
    They are used to add interest including sculptures, pools, fountains, rocks, furniture, and lighting.

## Slide 18: The Major Design Areas
The Outdoor Living Area
  What is the ceiling of the living area
    This can include overhead features
    Sky
    Trees provide the most common ceiling

## Slide 19: The Major Design Areas
The Outdoor Living Area
  What are the walls of the living area:
    Fences wooden or plastic
    Plants
    Stones and bricks

## Slide 20: The Major Design Areas
The Outdoor Living Area:
  What is the floor of the living area:
  The floor can be made out of many different materials
  The most common is the grass lawn
  Other surfaces include ground cover plants, organic mulches, inorganic mulches, concrete, stone, and brick pavers.

## Slide 21: The Major Design Areas
The Outdoor Living Area:
  Patios are built with hard permanent materials and are level with the ground. Common materials used are the brick pavers, concrete, and flagstone
  Decks are wooden surface areas raised above the ground level. Some materials are cedar, redwood, and wood treated to resist decay are used.

## Slide 22: The Major Design Areas
The Outdoor Living Area:
  Decks require more maintenance than a patio
  You will need to stain a deck every 3-4 years depending on the severity of the weather and the wood use
  Patios and Decks serve as a transition from the interior of the house to the outdoors
  They are both always located nearest to the kitchen for the ease of cooking outdoors

## Slide 23: The Major Design Areas
The Outdoor Living Area:
  Plantings
    The primary function of plants is to provide pleasure for the homeowner.
    Annuals and Perennials give a splash of color to the landscape
    Some plants are called high interest plantings where they are designed to capture the attention of the viewer and to provide interest to the garden

## Slide 24: The Major Design Areas
The Outdoor Living Area:
  Garden Accessories are items in the landscape that attracts attention and provide interest. Garden Accessories can also act as a focal point in the outdoor living area.
  Some accessories can include sculptures, pools, and lawn ornaments

## Slide 25: The Major Design Areas
The Service Area:
  are areas to the rear or the side of the house set aside for strictly functional purposes make up this area.
  Garbage cans, garden storage sheds, clotheslines, compost piles, and vegetable gardens

## Slide 26: The Major Design Areas
Service Area:
  The play area needs to blend in with the landscape. It is best to place the play areas where they are less noticeable

## Slide 27: The Major Design Areas
The End!!!
Any Questions!!